SPECIFICATION TEMPLATE

# IBOARD Rigid Insulation Board – Brick Cavity, Frame Wall & Concealed Soffit Applications

# Insulation Material:

# The brick cavity / frame wall / concealed soffit insulation shall be IBOARD ____ mm thick, with a thermal value of R____, comprising a closed-cell CFC/HCFC-free, zero ozone depletion potential (ODP), non-corrosive, zero formaldehyde content, rigid thermoset polyisocyanurate foam core with two reflective gas-tight aluminium foil facings, tested in accordance with AS/NZ standards to comply with the BCA/NCC and manufactured by Blue Chip Group Pty Ltd (Ph: 08 9451 2344).

**NO ALTERNATIVE MATERIALS WILL BE ACCEPTED FOR THIS PROJECT**

# Fire Properties:

# In accordance with NATA accredited AS 1530.3 fire testing which is the relevant testing in accordance with NCC 2019 specification C1.10 for concealed applications, IBOARD rigid insulation achieves the following results:

# •	Ignitability:		0

# •	Flame spread:		0

# •	Heat evolved:		0

# •	Smoke development:	2

# The IBOARD insulation shall be concealed inside a brick cavity wall, inside a plasterboard lined frame wall or behind a suspended ceiling in under slab soffit applications to comply with NCC 2019 requirements. If exposed insulation is required use IBOARD G1 or IBOARD F17.

# Thermal Performance:

# Thermal Conductivity: 		ASTM C518: 0.022 W/mK

# Emittance of Foil Facings:	ASTM-E408-71: 0.05

# Safety and Environmental:

# Insulation shall be 100% non-corrosive and comprised of a closed-cell CFC/HCFC-free and zero ozone-depletion potential (ODP) rigid thermoset polyisocyanurate foam core, manufactured using raw materials containing zero trace levels of formaldehyde.

# Technical Details:

# •	Bulk density:		± 32 kg/m3

# •	Compressive strength:	≥ 150 kPa (15 ton/m² at 10% deformation)

# •	Closed cells:		90-95% minimum

# •	Vapour diffusion:	PIR foam: μ = 60. ALU lamination: μ > 100,000

# Material R-Value

| IBOARD Thickness (mm) | 27 | 37 | 47 | 57 | 67 | 77 | 87 | 97 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Material R-Value | 1.23 | 1.68 | 2.14 | 2.59 | 3.05 | 3.50 | 3.95 | 4.41 |

Warranty:

IBOARD to be covered by manufacturer’s warranty for a minimum period of 10 years. All work to be carried out in accordance with the manufacturer's recommendations.

Disclaimer:

This Specification provided is generic in nature and is supplied in good faith for Specification guidance purposes only. It is understood that no 2 projects are alike and project specific information and advice should be obtained from necessary engineers, consultants and suppliers on a project to project basis.